## Slide 1
MASTER’S THESIS
Optimal experimental design using Bayesian optimization for kinetic parameter estimation with Reduced Order CFD models
Methanol synthesis from CO₂ hydrogenation
Reduced-order CFD · Reduced basis solver · Fisher-information design
CO₂ + 3H₂
⇌
CH₃OH + H₂O
Final defense
Presented by: Jahnavi Reddy Pocha (PEESE)
Guidance by: Muhammad Uzair Qureshi, M.Sc
Supervised by: Prof. Dr.-Ing.habil. Jens-Uwe Repke
Notes: Open with the central problem: reliable MeOH kinetics need informative experiments, but full CFD makes adaptive experiment design expensive.

## Slide 2
MOTIVATION
Kinetic estimation is limited by information and computation
02
The thesis addresses two coupled bottlenecks.
1. Limited information
Arbitrary conditions may not distinguish activation, adsorption, and rate terms.
Poorly selected experiments - Correlated or unidentifiable kinetic parameters
2. Expensive physics
Each candidate condition requires a nonlinear reacting-flow prediction.
OED becomes computationally impractical
Thesis response
ROM accelerates simulations; Bayesian OED selects the next informative experiment.
y = (d, θ) + ε
Design d controls composition, temperature, and pressure; θ contains the unknown kinetics.
Master’s thesis · Methanol case study
Inverse problem
Notes: Stress that speed alone is not the goal. The decision loop must be both physically credible and information efficient.
where:
y is the measured reactor output,
G is nonlinear forward-model function
theta is the unknown kinetic parameter vector,
d is the experimental design, -operating conditions
epsilon represents measurement noise.

## Slide 3
AIM AND CONTRIBUTION
ROM-enabled OED targets MeOH kinetic learning
03
Research question
C
Model
Use ROM and RBS representations of reacting transport in a 2D catalytic channel.
Estimate
Estimate nine positive MeOH kinetic parameters from noisy outlet compositions.
Design
Use GP-based Bayesian optimization and maximize D-optimal information.
Master’s thesis · Methanol case study
Notes: The contribution is the combined workflow: physics-based reduction, kinetic inversion, and optimal experimental design.
The thesis develops a fast, physics-based route to select experiments for methanol kinetic estimation.
Use three objectives:
Develop a ROM/RBS forward model for the reacting CO_2–H_2 system.
Estimate nine methanol kinetic parameters from noisy synthetic outlet data.
Select experimental conditions using Bayesian optimization and D-optimal information.

## Slide 4
METHANOL CASE STUDY
The MeOH reactor couples transport and surface reactions
04
Gas species
CO₂ H₂ H₂O
CH₃OH CO N₂
Surface reactions
CO₂ + 3H₂ ⇌ CH₃OH + H₂O
CO₂ + H₂ ⇌ CO + H₂O
2D catalytic channel
Catalyst patch
Inlet
Outlet
Parabolic gas velocity transports reactants to the catalyst; diffusion and surface kinetics determine outlet composition.
Master’s thesis · Methanol case study
CO2 hydrogenation follows methanol synthesis and reverse water gas shift pathways
Notes: Introduce the physical system before discussing computation. N2 is inert; CO2 hydrogenation follows methanol synthesis and RWGS pathways.
Parabolic hagen Poiseuille velocity = max at center 4u and 0 velocity at the walls

## Slide 5
Problem
Full CFD is too costly inside an OED loop
05
∇·(ρ v + ) = 0
= −ρ Σᵦ ∇Yᵝ
species mass-balance equation + multicomponent Fickian diffusion-flux law + nonlinear catalytic boundary kinetics
Why OED becomes difficult
• Each candidate design needs a new nonlinear reacting-flow solution.
• Parameter estimation requires repeated model evaluations.
• Requires many candidate objective evaluations.
~4,958 s
Fine-grid FOM benchmark
2.55×10⁻⁴ s
ROM online benchmark
Master’s thesis · Methanol case study
Notes: The timing values are from the ROM-paper benchmark and motivate the offline-online reduction. They are not a claim about the exact runtime of this thesis code.
Flow transports reactants.--Diffusive species mass flux , ∇ - Divergence operator
Diffusion.-- -Multicomponent diffusion coefficient,
Reaction of catalyst surface - - Normal diffusive flux to/from the catalyst
Nonlinear kinetics determine surface consumption and production.
The equations must be solved repeatedly during estimation and design.
A single full CFD simulation may be manageable. Hundreds or thousands of simulations inside parameter estimation or experimental design become computationally expensive.
Replace repeated expensive CFD calculations with a fast physics-based reduced-order model while retaining the important transport and reaction behavior along with intelligent experiment selection.
The timing values are from the ROM-paper benchmark and motivate the offline-online reduction. They are not a claim about the exact runtime of this thesis code.
Flow transports reactants.--"J" ^𝛼Diffusive species mass flux , ∇ - Divergence operator
Diffusion.-- 𝐷-Multicomponent diffusion coefficient,
Reaction of catalyst surface - "n·Jᵅ " - Normal diffusive flux to/from the catalyst
Nonlinear kinetics determine surface consumption and production.
The equations must be solved repeatedly during estimation and design.
A single full CFD simulation may be manageable. Hundreds or thousands of simulations inside parameter estimation or experimental design become computationally expensive.
Replace repeated expensive CFD calculations with a fast physics-based reduced-order model while retaining the important transport and reaction behavior along with intelligent experiment selection.

## Slide 6
REDUCED-ORDER CFD
ROM shifts transport offline and kinetics online
06
The zero-reaction solution supplies the transport background; basis responses represent the reaction-induced perturbation.
1. Zero reaction
Solve flow and multicomponent transport. catalytic reaction rates set to 0
2. Basis responses
Precompute reaction-related spatial modes.
3. Online solve
Slove small nonlinear kinetic system
4. Output
Recover outlet composition and concentration field.
Master’s thesis · Methanol case study
Notes: thesis uses both the asymptotic ROM and a fuller reduced-basis representation. The online model remains much cheaper than the full PDE system.
- Zero-reaction solution - Species field solved with catalytic reaction rates set to zero. It captures convection and diffusion only.
\(\phi_r\) - Reduced-basis response field
\(a_r\) - Online basis coefficient
thesis uses both the asymptotic ROM and a fuller reduced-basis representation. The online model remains much cheaper than the full PDE system.
Y_ZRS - Zero-reaction solution - Species field solved with catalytic reaction rates set to zero. It captures convection and diffusion only.
\(\phi_r\) - Reduced-basis response field
\(a_r\) - Online basis coefficient

## Slide 7
METHANOL KINETICS
Nine parameters define the coupled MeOH kinetic law
07
p₁–p₅ control rate/adsorption terms; p₆–p₉ control temperature-dependent effects. All are estimated simultaneously.
Master’s thesis · Methanol case study
Notes: implemented model:. The current Julia code maps p2 into the denominator and p6/p9 into temperature factors.
The outlet response is determined by two coupled Langmuir–Hinshelwood-type rates.
adsorption/inhibition contribution of surface species – D
cubic - dependence - methanol-forming rate - availability of free catalytic sites and adsorbed intermediates.
r - MeOH formation rate

## Slide 8
INVERSE PROBLEM
Nine kinetic parameters are estimated in log space
08
MeOH estimation setting
• 9 unknown kinetic parameters
• 6 measured outlet species
• 10 repeated measurements per experiment
• Noise levels: 10⁻⁵, 10⁻⁶, 10⁻⁷
• Initial designs: 10
• Maximum experiments: 150
The log transformation prevents parameters with vastly different magnitudes from dominating the optimizer.
Master’s thesis · Methanol case study
Notes: Explain synthetic-noise testing: because the true vector is known, estimation error can be measured directly. Real experimental data would require uncertainty intervals instead.
Parameter-estimation problem:- Nine positive kinetic parameters are estimated from repeated noisy outlet-composition measurements.
unknown kinetic parameter Estimator:
This avoids numerical imbalance between parameters spanning many orders of magnitude
Explain synthetic-noise testing: because the true vector is known, estimation error can be measured directly. Real experimental data would require uncertainty intervals instead.
Parameter-estimation problem:- Nine positive kinetic parameters are estimated from repeated noisy outlet-composition measurements.
Estimator:𝜃 ˆ
This avoids numerical imbalance between parameters spanning many orders of magnitude

## Slide 9
OPTIMAL EXPERIMENTAL DESIGN
D-optimal design selects informative experiments
09
High sensitivity
The outlet composition changes when a parameter changes. Large sensitivity is useful.
Low correlation
Different parameters alter the outputs in distinguishable ways. Independent parameter sensitivities are more useful than correlated sensitivities.
High information gain
The chosen condition contracts parameter uncertainty most strongly.
Master’s thesis · Methanol case study
Notes: The FIM is calculated by finite differences in normalized parameter space. The information objective is local and depends on the nominal parameter vector.
The best experiment is the one expected to distinguish the nine parameters most strongly.
Sensitivity matrix:J(d, )
Sensitivity Jacobian – J(d)
Fisher information matrix: F(d)
U(d)-- Fisher-information objective / utility - D-optimal information gain
P0 - Prior precision matrix
The FIM is calculated by finite differences in normalized parameter space. The information objective is local and depends on the nominal parameter vector.
The best experiment is the one expected to distinguish the nine parameters most strongly.
Sensitivity matrix:J(d, 𝜃)
Sensitivity Jacobian – J(d)
Fisher information matrix: F(d)
U(d)-- Fisher-information objective / utility - D-optimal information gain
P0 - Prior precision matrix

## Slide 10
BAYESIAN OPTIMIZATION
Bayesian optimization concentrates simulations where information is highest
10
EI balances exploitation of promising conditions with exploration of uncertain regions.
FIO defines the information objective; EI determines which candidate should be evaluated next.
Random sampling spends simulations without learning from previous experiments. Bayesian optimization updates its search strategy after every batch.
Evaluate
Calculate FIO utility for initial MeOH designs.
Learn
Fit a Gaussian-process surrogate. Quantify predicted utility and uncertainty.
Acquire
Use expected improvement to rank candidates and select the next design
Update
Run the selected batch, estimate parameters, and repeat.
Master’s thesis · Methanol case study
Notes: Clarify the distinction: Bayesian optimization searches experimental conditions d; the inner inverse problem estimates the parameter vector theta.
\(\mu(d)\): predicted objective value;
\(\sigma(d)\): uncertainty in that prediction.
- Best observed objective value
- Exploration parameter
- Standard normal CDF - Probability that the candidate improves on the current best value
- Standard normal PDF - Gives value to unexplored, uncertain regions
Each BO iteration selects a design, generates noisy MeOH data, updates kinetics, and proposes the next experiment.
A["Initial MeOH designs"] --> B["ROM/RBS forward model"] B --> C["Synthetic outlet data + Gaussian noise"] C --> D["Julia/Ipopt parameter estimation"] D --> E["FIM and D-optimal information"] E --> F["Gaussian-process surrogate"] F --> G["Expected-improvement acquisition"] G --> H["Next batch of four experiments"] H --> B
Clarify the distinction: Bayesian optimization searches experimental conditions d; the inner inverse problem estimates the parameter vector theta.
\(\mu(d)\): predicted objective value;
\(\sigma(d)\): uncertainty in that prediction.
𝑓_best - Best observed objective value
𝜉 - Exploration parameter
Φ(𝑧) - Standard normal CDF - Probability that the candidate improves on the current best value
𝜙(𝑧) - Standard normal PDF - Gives value to unexplored, uncertain regions
Each BO iteration selects a design, generates noisy MeOH data, updates kinetics, and proposes the next experiment.
A["Initial MeOH designs"] --> B["ROM/RBS forward model"] B --> C["Synthetic outlet data + Gaussian noise"] C --> D["Julia/Ipopt parameter estimation"] D --> E["FIM and D-optimal information"] E --> F["Gaussian-process surrogate"] F --> G["Expected-improvement acquisition"] G --> H["Next batch of four experiments"] H --> B

## Slide 11
COMPUTATIONAL WORKFLOW
The implementation closes the MeOH design loop
11
Initial designs
10 feasible MeOH conditions
ROM / RBS
Outlet compositions
Noisy data
10 repeats per experiment
Ipopt estimate
Update 9 kinetics
FIO + GP
Select the next batch
Repeat until the experiment budget is exhausted
Python: GP/EI, design handling, figures • Julia: VoronoiFVM ROM/RBS and constrained parameter estimation
Master’s thesis · Methanol case study
Notes: Use this slide for the code architecture. Explain that Python passes physical experiment arrays to Julia; scaled variables are used only inside the GP surrogate.

## Slide 12
ALGORITHMIC VERIFICATION ONLY
Mass-action verification precedes the MeOH study
12
r = k₁ exp()
Three species · one reaction · two unknown parameters
Purpose: verify BO–estimation integration
< 0.3%
Both parameters recovered at σ = 10⁻⁵ with RBS
Master’s thesis · Methanol case study
Notes: The mass-action model is a verification benchmark showing that the workflow can identify two known parameters under controlled conditions.
At \(\sigma=10^{-5}\), the RBS benchmark recovered both parameters within approximately \(0.3\%\). This establishes workflow feasibility; it does not prove nine-parameter methanol identifiability

## Slide 13
RESULTS
Mass Action Kinetic parameter convergence
24
Appendix · parameter-label quality control
Mass action kinetics FIO
Mass action kinetics RBS -
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 14
METHANOL EXPERIMENTAL DESIGN SPACE
The MeOH design space spans seven operating inputs
13
Feasible operating region
CO₂: 0.10–0.33
H₂: 0.10–0.25
H₂O: 0–0.01
CH₃OH: 0–0.01
CO: 0–0.30
T: 450–550 K
P: 15–50 bar
N₂ completes the inlet mass balance.
Master’s thesis · Methanol case study
Notes: The plotted design space is a 3D projection of a seven-dimensional design vector.
The OED search varies composition, temperature, and pressure within an experimentally feasible MeOH domain.

## Slide 15
RESULTS
MeOH parameter convergence
24
Appendix · parameter-label quality control
RBS
Random design:
Notes: Its design-selection rule is simply uniform random sampling over the feasible operating space

## Slide 16
FIO–RBS RESULTS
FIO utility increases under the 150-experiment budget
14
64.15
final information at σ=10⁻⁵
85.00
final information at σ=10⁻⁶
105.95
final information at σ=10⁻⁷
Master’s thesis · Methanol case study
Notes: Discuss the monotonic accumulation of information. Lower assumed measurement noise increases the information scale because the FIM is weighted by 1/sigma squared.
The FIO strategy systematically increases the expected information contained in the experiment set.

## Slide 17
PRIMARY RESULT
RBS improves MeOH kinetic-parameter recovery versus asymptotic ROM
15
Chart: RMS relative parameter error
| σ=10⁻⁵ | σ=10⁻⁶ | σ=10⁻⁷
FIO–RBS | 0.47798 | 0.27583 | 0.5245
FIO–asymptotic | 2.1915 | 2.7907 | 1.4163
RBS: 0.478, 0.276, 0.524 · Asymptotic: 2.192, 2.791, 1.416
Same FIO framework · same 150-experiment budget · same nine-parameter metric
Interpretation
• The fuller RBS representation gives lower total error at every tested noise level.
• The strongest case is σ=10⁻⁶: 0.276 versus 2.791.
• RBS improves the inverse solution even when the FIO design pathway is unchanged.
This is the central quantitative conclusion of the MeOH study.
Master’s thesis · Methanol case study
Notes: For the same FIO designs, the RBS estimator produces substantially lower overall error than the asymptotic ROM estimator.
it shows materially better recovery for the RBS (Reduced Basis Strategy more robust) estimator under this synthetic-design study.
For example, at \(\sigma=10^{-6}\), FIO-RBS estimates \(p_6\)–\(p_9\) within approximately \(0.3\%\)–\(4.4\%\), while \(p_1\)–\(p_5\) retain larger errors

## Slide 18
PARAMETER-WISE INTERPRETATION
MeOH identifiability is parameter-dependent
16
What the error pattern means
• Thermal terms p₆–p₉ are recovered relatively well.
• The MeOH rate/adsorption group p₁–p₅ remains much more uncertain.
• The problem is therefore dominated by parameter correlation—not simply by measurement noise.
Designs should be selected to separate parameter effects, not MeOH output
Master’s thesis · Methanol case study
Notes: Explain that several adsorption and pre-exponential terms can compensate one another in the outlet response.

## Slide 19
WHY FIO IS THE MAIN OED OBJECTIVE
High MeOH output is not automatically informative
17
Target-output BO maximizes CH₃OH outlet fraction. FIO maximizes parameter information. These are related objectives, but they are not equivalent.
Master’s thesis · Methanol case study
Notes: This slide explains why the thesis should foreground the FIO method: a high-yield condition may not separate the kinetic parameters well.
Selecting experiments for high methanol yield alone does not necessarily yield the best kinetic estimates.

## Slide 20
COMPARISON
Random experiments are the necessary OED baseline
18
FIO improves parameter recovery at lower noise.
FIO selects designs with explicitly high local parameter sensitivity.
The information objective increases as assumed measurement noise decreases.
At and
FIO gives lower parameter-recovery error than random at approximately the same budget.
Master’s thesis · Methanol case study
Noise level | FIO–RBS | Random–RBS | Preliminary outcome
 | 2.163 | 0.765 | Random is better at this checkpoint
 | 0.492 | 0.766 | FIO is better
 | 0.536 | 0.768 | FIO is better
Noise level | FIO–RBS | Random–RBS | Preliminary outcome
 | 2.163 | 0.765 | Random is better at this checkpoint
 | 0.492 | 0.766 | FIO is better
 | 0.536 | 0.768 | FIO is better
Notes: Be transparent: the random baseline is valuable, but the current outputs do not support an uncontrolled headline claim that BO universally beats random design. State the needed controlled reanalysis.
At an approximately equal experiment budget, FIO-based design reduced the RMS relative kinetic-parameter error at the two lower noise levels. The high-noise result was unstable, and the present comparison is preliminary because the two workflows must still be harmonized with respect to repeat count, initialization, exact budget, and multiple random seeds

## Slide 21
LIMITATIONS AND VALIDITY
The study demonstrates feasibility and clear limits
19
Local information
FIO is based on a nominal parameter vector. In the synthetic study, it is set to the true parameter vector.
Synthetic measurements
Known truth enables validation, but real-data uncertainty and model discrepancy are not yet represented.
ROM validity
The model is isothermal and is strongest for the small-reactive-perturbation regime.
Non-monotonic noise trend
Lower noise does not always lower error: nonconvexity and parameter correlation remain influential.
Parameter mapping
Rate-law parameter names must be made consistent across Julia, Python, plots, and thesis text.
Industrial extension
Heat effects, deactivation, and real measurement correlations remain future work.
Master’s thesis · Methanol case study
Notes: For a stronger Bayesian extension, use posterior samples rather than the true parameters.
Include these limitations:
In real experiments, true parameters are unknown.
Results are not monotonic with decreasing noise; this indicates nonconvexity, parameter correlation, model discrepancy, or optimizer/bound effects.
The ROM is isothermal and assumes conditions where the asymptotic reduction remains valid.
RBS improves recovery, but does not make every parameter identifiable.

## Slide 22
CONCLUSIONS
ROM-enabled FIO makes MeOH design practical
20
9
coupled MeOH kinetic parameters estimated
6
outlet species used as measurements
150
maximum MeOH experiments in BO/FIO runs
What this thesis establishes
• The ROM model enables repeated CFD-informed kinetic estimation.
• FIO provides an explicit criterion for selecting informative MeOH experiments.
• RBS gives substantially better parameter recovery than the asymptotic ROM in the present study.
• Parameter correlation remains the main obstacle to complete nine-parameter identifiability.
Master’s thesis · Final conclusion
Notes: feasibility and improvement are demonstrated; complete identifiability and real-experiment deployment remain future work.
ROM-enabled information-based experiment design is feasible for methanol kinetic estimation, with RBS providing the strongest current results.

## Slide 23
FUTURE WORK
Next: a fully adaptive real-data workflow
21
1
Update nominal θ
Use the current estimate or posterior rather than true synthetic parameters.
2
Quantify uncertainty
Report parameter correlations, confidence intervals, and posterior distributions.
3
Increase physical realism
Include energy balance, deactivation, and real experimental measurements.
The practical goal is not simply faster simulation—it is better experiments and more trustworthy MeOH kinetics.
Master’s thesis · Methanol case study
Which operating conditions make all nine MeOH kinetic parameters identifiable—not merely measurable?
Notes: Future work emphasize posterior updating and fair benchmarking, then physical extensions toward plant-relevant behavior.

## Slide 24
Thank you
Questions and discussion
Optimal experimental design using Bayesian optimization and Reduced Order CFD
Notes: Invite questions. Keep appendix slides available for detailed equations and parameter mappings.

## Slide 25
REFERENCE
Reference
24
Appendix · parameter-label quality control
[1] M.U. Qureshi, S. Matera, D. Runge, C. Merdon, J. Fuhrmann, J.-U. Repke, G. Brösigke, Reduced order CFD modeling approach based on the asymptotic expansion—An application for heterogeneous catalytic systems, Chemical Engineering Journal 504 (2025) 158684. https://doi.org/10.1016/j.cej.2024.158684
[2] K.M. Vanden Bussche, G.F. Froment, A steady-state kinetic model for methanol synthesis and the water-gas shift reaction on a commercial Cu/ZnO/Al(_2)O(_3) catalyst, Journal of Catalysis 161 (1) (1996) 1–10. https://doi.org/10.1006/jcat.1996.0156
[3] K. Chaloner, I. Verdinelli, Bayesian experimental design: A review, Statistical Science 10 (3) (1995) 273–304. https://doi.org/10.1214/ss/1177009939
[4] D.R. Jones, M. Schonlau, W.J. Welch, Efficient global optimization of expensive black-box functions, Journal of Global Optimization 13 (4) (1998) 455–492. https://doi.org/10.1023/A:1008306431147
[5] C.E. Rasmussen, C.K.I. Williams, Gaussian Processes for Machine Learning, MIT Press, Cambridge, MA, 2006. http://www.gaussianprocess.org/gpml/
[6] J. Fuhrmann, D. Abdel, J. Weidner, A. Seiler, P. Farrell, M. Liero, VoronoiFVM.jl: Finite volume solver for coupled nonlinear partial differential equations, 2023. https://doi.org/10.5281/zenodo.3529808
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 26
APPENDIX
Appendix: governing equations and catalyst boundary
23
∇·(ρv) = 0
∇·(ρv⊗v + pI − τ) = ρg
∇·(ρvYᵅ + Jᵅ) = 0
ρ = pref / [RT Σᵅ(Yᵅ/Mᵅ)]
Jᵅ = −ρ ΣᵝDᵅᵝ∇Yᵝ
at catalyst boundary
Appendix · ROM paper governing equations
Notes: Use only if asked for the full CFD formulation.
[Sources]
- Qureshi et al. (2025), uploaded ROM model-main paper.pdf

## Slide 27
APPENDIX
Appendix: MeOH parameter mapping
24
Group | Implemented role
p₁ | Methanol kinetic coefficient at
p₂ | hydrogen adsorption denominator coefficient
 | Hydrogen adsorption coefficient at
p₄ | Water adsorption coefficient at
p₅ | RWGS kinetic coefficient at
p₆ | Methanol temperature coefficient
p₇ | Temperature coefficient for
p₈ | Temperature coefficient for
p₉ | Positive magnitude associated with the RWGS temperature coefficient
Group | Implemented role
p₁ | 
p₂ | hydrogen adsorption denominator coefficient
p₄ | 
p₅ | 
p₆ | Methanol temperature coefficient
p₇ | 
p₈ | 
p₉ | Positive magnitude associated with the RWGS temperature coefficient
Appendix · parameter-label quality control
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 28
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: \(A_1\) is the pre-exponential rate coefficient for methanol formation

## Slide 29
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: activation energy – E1

## Slide 30
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: K_H_2: hydrogen adsorption coefficient

## Slide 31
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 32
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 33
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 34
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 35
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: This appendix is intentionally transparent about the current naming inconsistency. Resolve it before submission.
[Sources]
- thesis codes/src/reaction_kinetics.jl
- thesis codes/bayes_design_meoh_FIO_RBS_final.py

## Slide 36
APPENDIX
Appendix: RBS MeOH parameter convergence - Results
24
Appendix · parameter-label quality control
Random design
Notes: RWGS temperature coefficient